## Slide 1
FluvialGeomorph-Level 1:
Channel Slope and Cross-Section Analysis:
Plot Longitudinal Profile
- Spacing of points is critical for assessing channel
- Recommended options of 1 ft to 50 ft depending on analysis
Assess Longitudinal Profile
- Identify locations where channel slopes change dramatically
- Compare to existing LiDAR or channel surveys
Layout Cross Sections
- Layout regularly spaced cross sections for reach
- Recommended options of 50 ft depending on analysis
Assess Cross Section Geometry
- Extract cross section elevation values for profile plot analysis.
- Compare cross-section longitudinal profile locations
Repeat for each Study Area Extent
Level 1: FG Reports
- Reach reports for profile and cross-section analysis.
- Single or Multi-year analysis comparisons
Determine Appropriate Next Steps
- Proceed to Level 2 FG analysis
- Proceed with Other Geomorphic Analysis
- Focused Further Analysis of identified reaches
Select Study Area Extent
Single Reach
Small Watershed (HUC < 12)
Large Watershed (HUC > 12)

## Slide 2
FluvialGeomorph
Workflow:
Develop Regional Curves
Collect Gage Data
USGS-NWIS
Gage datum
Gage descriptions
Rating tables
Create Terrain
Create a DEM for each gage site.
Detrend DEM
Remove stream slope from terrain.
Define Channel Extent
Use detrended terrain to define channel extent.
Map Riffles
Identify location of riffle cross sections.
Calculate Riffle Geometry
Extract cross section elevation values and calculate hydraulic dimensions.
Select Region
Hydro-physiographic regions
Ecoregions
Identify Gage
> 10 year period of record
Active gages
Discontinued gages
Define Reach
Based on gage location
Determine reach extent
Reach length 20-30 bankfull widths
Use Hydraulic
Equations
Mannings or other equations
Compare cross sections
Average
Repeat for
each gage
site
Develop Hydraulic Geometry Relationships
Calculate bankfull channel dimensions
Develop Regional Curve
Plot bankfull channel dimensions versus drainage area