## Slide 1
FluvialGeomorph
Workflow:
Rapid Watershed Assessment for Un-Gaged Streams
Create Terrain
Create a DEM for study area.
Define Watershed Reaches
Segment network into reaches with homogeneous drainage area.
Detrend DEM
Remove the stream slope from the terrain.
Define Channel Extent
Use the detrended terrain to define the channel extent.
Map Riffles
Identify the location of riffle cross sections.
Calculate Riffle Geometry
Extract elevation values for cross sections and calculate hydraulic dimensions.
Estimate Bankfull
Compare current cross section to regional curve values to select bankfull elevation.
Layout Cross Sections
Layout regularly spaced cross sections for reach.
Calculate Cross Section Geometry
Extract cross section elevation values and calculate hydraulic dimensions.
Calculate Planform Geometry
Calculate planform metrics for reach.
Repeat for each watershed reach

## Slide 2
FluvialGeomorph
Workflow:
Develop Regional Curves
Collect Gage Data
USGS-NWIS
Gage datum
Gage descriptions
Rating tables
Create Terrain
Create a DEM for each gage site.
Detrend DEM
Remove stream slope from terrain.
Define Channel Extent
Use detrended terrain to define channel extent.
Map Riffles
Identify location of riffle cross sections.
Calculate Riffle Geometry
Extract cross section elevation values and calculate hydraulic dimensions.
Select Region
Hydro-physiographic regions
Ecoregions
Identify Gage
> 10 year period of record
Active gages
Discontinued gages
Define Reach
Based on gage location
Determine reach extent
Reach length 20-30 bankfull widths
Use Hydraulic
Equations
Mannings or other equations
Compare cross sections
Average
Repeat for
each gage
site
Develop Hydraulic Geometry Relationships
Calculate bankfull channel dimensions
Develop Regional Curve
Plot bankfull channel dimensions versus drainage area